## Slide 1
San Diego County: Towards a Reliable and Sustainable Public Transportation System
Franco Boscolo
Research Associate, Global Energy Network Institute (GENI)
Under the supervision of
Peter Meisen
President, Global Energy Network Institute (GENI)

## Slide 2: Summary
Fleet information
Population trends
Suggestion for a more reliable system
Suggestion for a more sustainable system

## Slide 3: Fleet information
MTS
    Bus
    Trolley
NCTD
    BREEZE
    COASTER
    SPRINTER
Amtrak
    Pacific Surfliner
Notes: MTS: Metropolitan Transit System
NCTD: North County Transport District

## Slide 4
Population trends
Chart: 
| Driving Alone | Carpooling | Work at home | Public Transits | Walking | Other
% | 0.76 | 0.1 | 0.06 | 0.03 | 0.03 | 0.02
Modes of commuting to work (2010)

## Slide 5
Population trends
Chart: miles
| San Francisco | Los Angeles | Orange County | San Diego | CALIFORNIA
2009 | 4.3 | 10.2 | 12.2 | 13.5 | 12.7
2010 | 4.5 | 10.5 | 12.2 | 14.5 | 13
Daily Vehicle Miles Travelled (VMT) per capita
Notes: San Diego:
13.5 miles in 2009
14.5 miles in 2010
California:
12.7 miles in 2009
13 miles in 2010

## Slide 6
Population trends
Chart: Millions of miles
| 1983 | 1985 | 1987 | 1989 | 1991 | 1993 | 1995 | 1997 | 1999 | 2001 | 2003 | 2005 | 2007
 | 29 | 33 | 39 | 44.7 | 45 | 46 | 48 | 49 | 51 | 56 | 57 | 62 | 61
Daily Vehicle Miles Travelled (VMT)
Notes: 2005: 62 millions
2007: 61 millions
Actual: more than 60 millions

## Slide 7
Population trends
Chart: Millions of ridership
| New York City | Chicago | San Francisco | Los Angeles | Washington | San Diego
Ridership | 508 | 480 | 440 | 430 | 390 | 75
Transit ridership by city
Notes: NYC: 508
SD: 75

## Slide 8
Population trends
Chart: 
| 2008 | 2020 | 2030 | 2035 | 2050
Population | 3131552 | 3535000 | 3870001 | 4026131 | 4384867
Jobs | 1501080 | 1604615 | 1752630 | 1798372 | 2003038
Housing | 1140654 | 1262488 | 1369797 | 1417520 | 1529090
Population, jobs and housing growth
Notes: 2008: Population 3,131,552: Jobs 1,501,080; Housing 1,140,654
Current (2011): Population 3,140,069
2050: Population 4,384,867; Jobs 2,003,038; Housing 1,529,090

## Slide 9
Proposal: reliable system
Comparison of perception of mode performance

## Slide 10
Proposal: reliable system
Chart: 
| No travels to necessary areas | Stops locations are inconvenient | General inconvenience of transit | Takes too long | No transit options near home | Schedule inconvenient | Prefer other modes | Too expensive | Do not need / Rarely travel | Other
 | 20.2 | 15 | 13.9 | 10.8 | 9.8 | 8.5 | 8 | 5.1 | 4.2 | 4.5
Motivations for not using transits

## Slide 11
Proposal: reliable system
2050 regional development plan
Area improvement
Transit development
Fast connections

## Slide 12
Proposal: reliable system
Chart: seconds
| 12th & Imperial | 12th & Petco Pk. | 12th & K | Park & J | Park & Island | Park & Market | Park & G | Park & F | Park & E | Park & Brodway | C & 11th | C & 10th | C & 9th | C & 8th | C & 7th | C & 6th | C & 5th | C & 4th | C & 3rd | C & 2nd | C & First | C & Front | C & India | Average
Red light time (s) | 38 | 28 | 22 | 20 | 25 | 27 | 40 | 34 | 20 | 17 | 39 | 27 | 44 | 35 | 36 | 28 | 32 | 36 | 36 | 35 | 39 | 40 | 47 | 32.3913
Bus lanes and automatic light systems
Toll lanes on highways
Bus lanes on city centres
Active signal priority system

## Slide 13
Proposal: reliable system
More transit options
Higher transit frequency

## Slide 14
Proposal: reliable system
GPS-tracked transits:
Online and mobile Apps:

## Slide 15
Proposal: sustainable system
Chart: g/km
| CO | NOx | PM
Euro3 Diesel | 7.15 | 17.01 | 0.34
Early CNG | 5.33 | 12.17 | 0.02
Diesel vs. Compressed Natural Gas (CNG)
Reduction: 25.45% 28.45% 98.12%

## Slide 16
Proposal: sustainable system
Diesel vs. Compressed Natural Gas (CNG)
Source | Emissions (gCO2eq/km) |  | 
 | Diesel | CNG | Reduction
Beer et al. 2001 | 1,759 | 1,604 | 8.81%
Sliva et al. 2006 | 2,277 | 2,070 | 9.09%
Cost Details | CNG ($) |  | Clean Diesel ($) | 
 | Per Bus | Per Fleet | Per Bus | Per Fleet
Incremental CNG Fuel | 2,860 | 0.6 x 106 | - | -
CNG Fuel Station Maintenance | - | 0.9 x 106 | - | -
Incremental Bus Maintenance | 5,200 | 1.0 x 106 | - | -
Incremental Cleaning Technology | - | - | 1,040 | 208,000
Diesel Fuel Station Maintenance | - | - | - | 92,000
Clean Technology Replacement | - | - | 137 | 27,400
Annual Technology Cleaning | - | - | 670 | 134,000
TOTAL |  | 2,500,000 |  | 461,400
When both engine types are retrofitted with cleaning technologies, reductions decrease
Costs do not justify CNG choice:
Notes: Examples:
Catalitic reduction
Particulate filters

## Slide 17
Proposal: sustainable system
Electrification of the railway system
Service | Company | Travel (mi) | Weekly Trips | Yearly Travel (mi)
Coaster | NCTD | 41 | 46 | 98,072
Sprinter | NCTD | 22 | 132 | 151,008
Pacific Surfliner | Amtrak | 63 | 154 | 504,504
Total |  |  |  | 753,584
Rail and light-rail services powered by Diesel engines:
Electrification has the benefits of:
  - Reducing environmental impacts
  - Improving the reliability of the service
  - Increasing the capacity of trains
  - Reducing maintenance, fuel and wear and tear costs

## Slide 18
Proposal: sustainable system
Chart: CO2 Emissions (g/mi)
| Electric | Diesel
CO2 per vehicle mile (g) | 1664 | 2100
Chart: Distance (miles)
| Intercity | Regional
Electric | 16571 | 30209
Diesel | 11800 | 12880
CO2 reduction by electrification: 20% - 35% (no local)
Reliability improvement by electrification: 29% - 57%
Reduced operating costs (35%) and leasing costs (20%)

## Slide 19
Proposal: sustainable system
Regenerative braking system

## Slide 20
Proposal: sustainable system
Cycling and walking
Type | Miles | %
Bike Path | 159.3 | 11.9
Bike Lane | 890.2 | 66.4
Bike Route | 243.9 | 18.2
Freeway Shoulders | 47.4 | 3.5
Total | 1340.8 | 100
Current San Diego availability
Development of more bike and pedestrian paths
Development of a bike docking station system
Notes: 400 hiring docking points
6,000 bicycles
2000-2010 number of cyclists doubled
Development plan: 400% increase by 2026